Bootem Open Bootloader Protocol v1.0
# Introduction
The BOBP is designed to be simple, portable and reliable. These attributes have priority over speed, or support for proprietary features.
The protocol can be used over any comms connection that supports 8 bit data. For example, COM port, USB serial.
It is easy to implement on the host side, as the host downloader does not need to know any details of target, and does not need a database containing details of page sizes and addresses. The downloader needs to read a binary file, and read/write a serial connection.
On the target side, the bootloader can be small and simple. The bootloader knows details of where user flash is located, how big pages are, how to erase them etc.
Bootem is Open Source.

## Terms:
host	a device that runs the downloader. Typically a PC.
Target	a device that is to be programmed with user code and runs the bootloader, e.g. microcontroller
downloader	program running in the host that sends program code
bootloader	program running on the target that receive program code from the host
user code	program code representing the user application

Typical target memory:

reset address → Bootloader
user code address → User code
top of Flash →

# General Packet Format
Command format (sent by host)

FLAG
CMD
[DATA]
CRC
FLAG

Response Format (sent by target)

FLAG
RESPONSE
[DATA]
CRC
FLAG

Data between FLAG bytes must not contain FLAG or ESCAPE byte.
FLAG = 0x7E
ESCAPE = 0x7D
To escape a data byte, send 0x7D (data XOR 0x20)

0x7e is encoded as 0x7d, 0x5e.
0x7d is encoded as 0x7d, 0x5d.

Format for UART is 8 bit, no parity, 1 stop bit.
Baud rate should be 115200

CRC is 2's complement sum of all bytes except enclosing FLAG bytes.

If an unescaped FLAG byte is received,
If packet is invalid according to the CRC, it is ignored.

# Commands
0x01	Get Commands supported
0x02	Get Version
0x03	Get Part ID

0x10	Read Memory
0x20	Write User Flash
0x30	Erase User Flash
0x40	Enter Programming Mode
0x41	Exit Programming Mode
0x42	Execute user code (if valid)

# Responses
0x01
…
0x7F	Valid command complete OK.

If bit 7 is set, an error occurred:

0x80	invalid command (not supported)
0x81	invalid request (bad parameters)
0x82	invalid mode (erase or write command when not in programming mode)

## Get Info

Command

CMD = 0x01
DATA = []

Response

RES = 0x01
DATA = [commands supported]

## Get Version

RES = 0x02
DATA = [0x42, 0x4F, 0x42, 0x50, PROTO_MAJOR, PROTO_MINOR, BL_MAJOR, BL_MINOR]

0x42, 0x4F, 0x42, 0x50 is the signature “BOBP”.

PROTO_MAJOR, PROTO_MINOR is the version of BOBP supported. Implementations conforming to this specification MUST return 0x01, 0x00.
BL_MAJOR, BL_MINOR	is the version of target bootloader.
## Get Part ID

RES = 0x03
DATA = [Part ID bytes...]

## Read Memory

CMD = 0x10
DATA = [address 4 bytes (MSB)
length 2 bytes (MSB)
]

RES = 0x10
DATA = [memory data]

## Write User Flash
CMD = 0x20
DATA = [offset 4 bytes (MSB), data]

RES = 0x20
DATA = []

Not allowed unless in programming mode.
## Erase User Flash
CMD = 0x30
DATA = []

RES = 0x30 | error
DATA = []

Not allowed unless in programming mode.

## Enter Programming Mode
CMD = 0x40
DATA = []

RES = 0x40 | error
DATA = []

The target device is prepared for programming, e.g. by unlocking Flash containing user code. Commands to erase and write flash are enabled.

## Exit Programming Mode
CMD = 0x41
DATA = []

RES = 0x41 | error
DATA = []

The target is prepared for running user code, e.g. programming buffers are written, Flash locked to prevent accidental overwriting.
## Execute User Code
CMD = 0x42
DATA = []

RES = 0x42 | error
DATA = []